## Slide 1: Example

## Slide 2
Central Processing Unit 2 Lecture 22
CSE 211, Computer Organization and Architecture
Overview
Peripheral Devices
Input-Output Interface
Asynchronous Data Transfer
Modes of Transfer
Priority Interrupt
Direct Memory Access
Input-Output Processor
Serial Communication

## Slide 4
Input/Output Organization 4
Input Output Organization
  I/O Subsystem
  Efficient Mode Of Communication
    between central system and outside environment
  Programmed, Input Data, Process, Record, Display Results.
  Slow Keyboard Processor Idles Waiting For Slow Input.
  time of waiting is more for information to arrive
  E.G. Magnetic Tapes, Disks

## Slide 5
Input/Output Organization 5
Peripheral Devices
Devices under direct control of computer are
connected on-line.
Peripherals I/O devices attached to the computer
There are three types of peripherals :
  Input peripherals
  Output peripherals
  Input-output peripherals

## Slide 6
Input/Output Organization 6
Peripheral Devices
  Peripheral (or I/O Device)
      Monitor (Visual Output Device) : CRT, LCD
      KeyBoard (Input Device) : light pen, mouse, touch screen, joy stick, digitizer
      Printer (Hard Copy Device) : Daisy wheel, dot matrix and laser printer
      Storage Device  Magnetic tape, magnetic disk, optical disk

## Slide 7
Input/Output Organization 7
Peripheral Devices
Input Devices
Keyboard
Optical input devices
- Card Reader
- Paper Tape Reader
- Bar code reader
- Optical Mark Reader
Magnetic Input Devices
- Magnetic Stripe Reader (ATM)
Screen Input Devices
- Touch Screen
- Light Pen
- Mouse
Output Devices
Card Puncher, Paper Tape Puncher
CRT
Printer (Daisy Wheel, Dot Matrix, Laser)
Plotter

## Slide 9
Input/Output Organization 9
Input Output Organization
  ASCII (American Standard Code for Information Interchange)
    I/O communications usually involves data transfer
    Alphanumeric information from device and the computer.
    Standard binary code for alphanumeric character is ASCII
    ASCII Code :
      It uses 7 bits to code 128 characters (94 printable and 34 non printing)
      7 bit - 00 - 7F ( 0 - 127 )

## Slide 10
Input/Output Organization 10
Input Output Organization
  ASCII (American Standard Code for Information Interchange)
    ASCII is 7 bits but,
    most computers manipulate 8 bit quantity as a
    single unit called byte.
        80 - FF ( 128 - 255 ) : Greek, Italic type font
    Three types of control characters: Format effectors, Information separators and communication control

## Slide 11
Input/Output Organization 11
Input Output Organization
Format effectors control printing layout.
  Examples: backspace (BS), horizontal tab (HT),
  Carriage return (CR) is also included.
Information separators divide data sections, divisions like paragraphs and pages.
  Examples: record (RS), file separator (FS).
Communication control: transmission of text between remote terminals STX(Start of text) and ETX(end of text).

## Slide 13
Input/Output Organization 13
I/O Interface
Provides a method for transferring information
Transfer between internal storage and external I/O devices
(such as memory and CPU registers)
Resolves the differences between the computer and peripheral devices
  (1). Peripherals – Electromechanical or Electromagnetic Devices
  CPU or Memory - Electronic Device
      Conversion of signal values required

## Slide 14
Input/Output Organization 14
I/O Interface
  (2). Data Transfer Rate
    Peripherals - Usually slower
    CPU or Memory - Usually faster than peripherals
      Some kinds of Synchronization mechanism may be needed
  (3). Data formats or Unit of Information
    Peripherals – Byte, Block, …
    CPU or Memory – Word
  (4). Operating modes of peripherals may differ
    must be controlled so that not to disturbed other peripherals connected to CPU

## Slide 15
Input/Output Organization 15
I/O Bus and Interface
Processor
Interface
Keyboard
and
display
terminal
Magnetic
tape
Printer
Interface
Interface
Interface
Data
Address
Control
Magnetic
disk
I/O bus

## Slide 16
Input/Output Organization 16
I/O Bus and Interface
Interface :
- Decodes the device address (device code)
- Decodes the commands (operation)
- Provides signals for the peripheral controller
- Synchronizes the data flow and supervises
the transfer rate between peripheral and CPU or Memory
4 types of command interface can receive : control, status, data o/p and data i/p

## Slide 17
Input/Output Organization 17
I/O Bus and Interface
Control command :
  issued to activate peripheral and to inform what to do
Status command :
  used to test various status condition in interface and peripherals
data o/p command :
  causes the interface to respond by transferring data
  From the bus into one of its registers
data i/p command :
  interface receives an item of data from the peripheral
  Then, places it in its buffer register.

## Slide 18
Input/Output Organization 18
I/O Bus and Memory Bus
  MEMORY BUS is for information transfers between CPU and the MM
  I/O BUS is for information transfers.
  Transfer between CPU and I/O devices through their I/O interface
Functions of Buses

## Slide 19
Input/Output Organization 19
I/O Bus and Memory Bus
  3 ways to bus can communicate with memory and I/O :
  (1). use two separate buses,
  one to communicate with memory , the other with I/O interfaces
  - Computer has independent set of data, address and control bus
  - one for accessing memory and another I/O.
  - done in computers that have separate IOP other than CPU.
  (2). Use one common bus for memory and I/O but separate control lines
  for each
  (3). Use one common bus for memory and I/O with common control
  lines for both

## Slide 21
Input/Output Organization 21
Isolated vs. Memory Mapped I/O
- Many computers use common bus to transfer information between memory or I/O.
- The distinction between memory transfer and I/O transfer is made through separate read and write line.
-In the isolated I/O configuration ,
the CPU has distinct input and output instructions and each of these instruction is associated with the address of an interface register.
Distinct input and output instructions
  each associated with address of interface register
Isolated I/O

## Slide 22
Input/Output Organization 22
Isolated vs. Memory Mapped I/O
Memory-mapped I/O
  - A single set of read/write control lines
  (no distinction between memory and I/O transfer)
  - Memory and I/O addresses share the common address space
  -> reduces memory address range available
  - No specific input or output instruction
  -> The same memory reference instructions can
  be used for I/O transfers
  - Considerable flexibility in handling I/O operations

## Slide 23
Input/Output Organization 23
I/O Interface
- Information in each port can be assigned a meaning depending on the mode of operation of the I/O device→ Port A = Data; Port B = Command;
- CPU initializes(loads) each port by transferring a byte to the Control Register
→ Allows CPU can define the mode of operation of each port
→ Programmable Port: By changing the bits in the control register, it is possible to change the interface characteristics
CS RS1 RS0 Register selected
0 x x None - data bus in high-impedence
1 0 0 Port A register
1 0 1 Port B register
1 1 0 Control register
1 1 1 Status register
Programmable Interface
Chip select
Register select
Register select
I/O read
I/O write
CS
RS1
RS0
RD
WR
Timing
and
Control
Bus
buffers
Bidirectional
data bus
Port A
register
Port B
register
Control
register
Status
register
I/O data
I/O data
Control
Status
Internal bus
CPU
I/O
Device

## Slide 24
Input/Output Organization 24 Lecture 36
Peripheral Devices
Input-Output Interface
Asynchronous Data Transfer
Modes of Transfer
Priority Interrupt
Direct Memory Access
Input-Output Processor

## Slide 25
Asynchronous Data Transfer
Synchronous Data Transfer:
  Uses a common clock for all registers.
  Data transfer occurs simultaneously with clock pulses.
  CPU and I/O Interface operate independently but share a clock for transfer.
  Asynchronous Data Transfer:
  Each unit (CPU & Interface) has its own independent clock.
  Control signals are required to synchronize data transfer
  Each unit uses its own private clock for internal registers.
  Asynchronous data transfer between two independent units requires that control signals

## Slide 26
Asynchronous Data Transfer
  Two methods:
  STROBE: A control signal indicates when data is transmitted.
  HANDSHAKING: A mutual agreement between units for data transfer

## Slide 27
1
2
Source initiated strobe:
1
2

## Slide 28
1
2
Destination initiated strobe:
2
1

## Slide 29
Source initiated handshaking:

## Slide 30
    Timeout : If the return handshake signal does not respond within a given time period, the unit assumes that an error has occurred.

## Slide 31
  Asynchronous Serial Transfer
    Synchronous transmission :
      The two unit share a common clock frequency
      Bits are transmitted continuously at the rate dictated by the clock pulses
    Asynchronous transmission :
      Binary information sent only when it is available and line remain idle otherwise
      Special bits are inserted at both ends of the character code
      Each character consists of three parts :
        1) start bit : always “0”, indicate the beginning of a character
        2) character bits : data
        3) stop bit : always “1”

## Slide 32
    Asynchronous transmission rules :
       When a character is not being sent, the line is kept in the 1-state
       The initiation of a character transmission is detected from the start bit, which is always “0”
       The character bits always follow the start bit
       After the last bit of the character is transmitted, a stop bit is detected when the line returns to the 1-state for at least one bit time
    Baud Rate : Data transfer rate in bits per second
      10 character per second with 11 bit format = 110 bit per second

## Slide 33
Input/Output Organization 33
Universal Asynchronous Receiver Transmitter
A typical asynchronous communication interface available as an IC
Transmitter Register
- Accepts a data byte(from CPU) through the data bus
- Transferred to a shift register for serial transmission
Receiver Register
- Receives serial information into another shift register
- Complete data byte is sent to the receiver register
Status Register Bits
- Used for I/O flags and for recording errors
Control Register Bits
- Define baud rate, no. of bits in each character, whether to generate and check parity, and no. of stop bits
Chip select
I/O read
I/O write
CS
RS
RD
WR
Timing
and
Control
Bus
buffers
Bidirectional
data bus
Transmitter
register
Control
register
Status
register
Receiver
register
Shift
register
Transmitter
control
and clock
Receiver
control
and clock
Shift
register
Transmit
data
Transmitter
clock
Receiver
clock
Receive
data
CS RS Oper. Register selected
0 x x None
1 0 WR Transmitter register
1 1 WR Control register
1 0 RD Receiver register
1 1 RD Status register
Internal Bus

## Slide 34
UART stands for?
a. Universal Asynchronous Sender Receiver
b. Universal Asynchronous Receiver Transmitter
c. Universal Synchronous Receiver Transmitter
d. None Of These.

## Slide 35
Overview
Peripheral Devices
Input-Output Interface
Asynchronous Data Transfer
Modes of Transfer
Priority Interrupt
Direct Memory Access
Input-Output Processor

## Slide 36
Binary information received from external device is usually stored in memory.
Information transferred from central computer into an external device originates in the memory unit.
The CPU merely execute I/O instructions and may accept data temporarily but ultimate source or destination is the Memory Unit.
Modes of Transfer

## Slide 37
Data transfer between central computer and I/O devices may be handled in a variety of modes.
Some modes use CPU as intermediate path,
  others transfer data directly to and from memory unit.
Data Transfer to or from peripheral can be handled in one of three possible modes :
  Programmed I/O
  Interrupt-Initiated I/O
  Direct Memory Access (DMA)
Modes of Transfer

## Slide 38
Input/output Organization 38
Modes of Transfer – Programmed I/O

## Slide 40: Programmed I/O
- Programmed I/O operations are the result of I/O Instructions written in computer program.
- Each data item transfer is initiated by an instruction in the program.
Usually, transfer is to and from a CPU register to peripheral.
Other instructions are needed to transfer data to and from CPU and Memory
Transferring data under program control requires constant monitoring of the peripheral by CPU.

## Slide 41
In programmed I/O method,
  CPU stays in a program loop until the I/O unit indicated that it is ready for data transfer.
  This is a time consuming process since it keeps the processor busy needlessly.
  It can be avoided by using Interrupt facility and special commands
  Interrupt to inform the interface to issue an interrupt request signal when data are available for the device.

## Slide 42: Interrupted I/O
In the programmed I/O method, the CPU stays in a program loop until the I/O unit indicates that it is ready for data transfer.
This is a time-consuming process since it keeps the processor busy needlessly.
It can be avoided by using an interrupt facility and special commands to inform the interface to issue an interrupt request signal when the data are available from the device.
In the meantime the CPU can proceed to execute another program. The interface meanwhile keeps monitoring the device.

## Slide 43: Interrupted I/O
When the interface determines that the device is ready for data transfer, it generates an interrupt request to the computer.
Upon detecting the external interrupt signal, the CPU momentarily stops the task it is processing,
Then, Branches to a service program to process the I/O transfer, and then returns to the task it was originally performing.

## Slide 44
DMA
Programmed I/O: In this method, data moves between the CPU and external devices (like a keyboard, printer, or hard drive). The CPU controls the entire process.
Direct Memory Access (DMA): Instead of the CPU handling data transfer, a special hardware unit (DMA controller) transfers data directly between memory and external devices.
CPU’s Role in DMA: The CPU starts the transfer by giving the DMA controller a memory address and the amount of data to transfer. Then, the CPU moves on to other tasks.
How DMA Works: When the DMA is ready to transfer data, it requests permission to use the memory bus (the pathway between memory and other parts of the system).
Notes: DMA is more efficient for large data transfers since it frees the CPU and speeds up the process.
Interrupt-Initiated I/O is simpler but can slow down the CPU, making it less suitable for handling large amounts of data.

## Slide 45
DMA
Memory Controller’s Role: Once the memory controller allows access, the DMA controller moves data directly between the external device and memory.
Effect on CPU: The CPU temporarily pauses its memory operations while DMA transfers data but resumes immediately after.
Why This Matters: Since most external devices (like hard drives) work much slower than the CPU, these data transfers happen less frequently compared to how often the CPU accesses memory.
This approach allows the CPU to work on other tasks while data transfer happens in the background, improving overall system efficiency.
Notes: DMA is more efficient for large data transfers since it frees the CPU and speeds up the process.
Interrupt-Initiated I/O is simpler but can slow down the CPU, making it less suitable for handling large amounts of data.

## Slide 46
Priority Interrupts
Priority
- Determines which interrupt is to be served first,
  when two or more requests are made simultaneously
- Also determines which interrupts are permitted to interrupt the computer,
  while another is being serviced
- Higher priority interrupts can make requests while servicing a lower priority
interrupt

## Slide 47
Priority Interrupts
A priority interrupt is a system that establishes priority over the various sources to determine
- which condition is to serviced first when two or more requests
arrive simultaneously
-which conditions are permitted to interrupt the computer while
another request is being serviced

## Slide 48
Priority Interrupts
Priority Interrupt by Software (Polling)
Polling procedure is used to identify highest priority source by software
means
- common branch address for all the interrupts
- Priority is established by the order of polling the devices(interrupt sources)
- highest priority device is tested first and if interrupt is on ,
- control branches to service routine for this source otherwise next lower priority source is tested

## Slide 49
Priority Interrupts
- Flexible since it is established by software
- Low cost since it needs a very little hardware
- Very slow
- if there are many interrupt time required to poll may exceed time available to
service IO device

## Slide 50
Priority Interrupts
Priority Interrupt by Hardware
- Require a priority interrupt manager which accepts all the interrupt requests
to determine the highest priority request
- Fast since identification of the highest priority interrupt request is identified by
the hardware
- Fast since each interrupt source has its own interrupt vector to access
directly to its own service routine
- Can be addressed using serial or parallel connection of interrupt lines.
Example of serial is Daisy chaining Priority

## Slide 51
Hardware Priority Interrupts – Daisy Chain
Device 1
PI
PO
Device 2
PI
PO
Device 3
PI
PO
INT
INTACK
Interrupt request
Interrupt acknowledge
To next
device
CPU
VAD 1
VAD 2
VAD 3
* Serial hardware priority function
* Interrupt Request Line
- Single common line
* Interrupt Acknowledge Line
- Daisy-Chain
Serial connection of all device that request an interrupt
Device with highest priority placed in first position followed by devices with lower priority and so on.
Interrupt generated by any device  signals low state interrupt line
CPU responds by enabling interrupt acknowledgement (INTACK) line.
device receives PI=1 and passes to next only when not requesting else PI=0
Thus device with PI=1 and PO=0 is one with highest priority requesting interrupt

## Slide 52
Hardware Priority Interrupts – Daisy Chain
Example: Daisy chain working

## Slide 53
Hardware Priority Interrupts – Daisy Chain

## Slide 54
Parallel Priority Interrupts
Mask
register
INTACK
from CPU
Priority
encoder
I
0
I
1
I
2
I
3
0
1
2
3
y
x
IST
IEN
0
1
2
3
0
0
0
0
0
0
Disk
Printer
Reader
Keyboard
Interrupt register
Enable
Interrupt
to CPU
VAD
to CPU
Bus
Buffer
IEN: Set or Clear by instructions ION or IOF
IST: Represents an unmasked interrupt has occurred. INTACK enables tristate Bus Buffer to load VAD generated by the Priority Logic
Interrupt Register:
- Each bit is associated with an Interrupt Request from different Interrupt Source - different priority level
- Each bit can be cleared by a program instruction
Mask Register:
- Mask Register is associated with Interrupt Register
- Each bit can be set or cleared by an Instruction

## Slide 55
Priority Encoder
Determines the highest priority interrupt when more than one interrupts take place
Priority Encoder Truth table
1 d d d
0 1 d d
0 0 1 d
0 0 0 1
0 0 0 0
I0
I1
I2
I3
0 0 1
0 1 1
1 0 1
1 1 1
d d 0
x y IST
x = I0' I1'
y = I0' I1 + I0’ I2’
(IST) = I0 + I1 + I2 + I3
Inputs
Outputs
Boolean functions

## Slide 56
Interrupt Cycle
At the end of each Instruction cycle
- CPU checks IEN and IST
- If IEN  IST = 1, CPU -> Interrupt Cycle
  SP SP - 1 Decrement stack pointer
  M[SP]  PC Push PC into stack
  INTACK  1 Enable interrupt acknowledge
  PC  VAD Transfer vector address to PC
  IEN  0 Disable further interrupts
  Go To Fetch to execute the first instruction
  in the interrupt service routine

## Slide 57
Initial and Final Operations
JMP PTR
JMP RDR
JMP KBD
JMP DISK
0
1
2
3
Program to service
magnetic disk
Program to service
line printer
Program to service
character reader
Program to service
keyboard
DISK
PTR
RDR
KBD
255
256
750
256
750
Stack
Main program
current instr.
749
KBD
interrupt
2
VAD=00000011
3
4
Disk
interrupt
5
6
7
8
9
10
11
1
Initial and Final Operations
Each interrupt service routine must have an initial and final set of
operations for controlling the registers in the hardware interrupt system
Initial Sequence
[1] Clear lower level Mask reg. bits
[2] IST <- 0
[3] Save contents of CPU registers
[4] IEN <- 1
[5] Go to Interrupt Service Routine
Final Sequence
[1] IEN <- 0
[2] Restore CPU registers
[3] Clear the bit in the Interrupt Reg
[4] Set lower level Mask reg. bits
[5] Restore return address, IEN <- 1

## Slide 58
In Daisy Chaining Priority if the device does not have any pending interrupt requests then the value of PI and PO will be
a. PI=0, PO=0
b. PI=0, PO=1
c. PI=1, PO=0
d. PI=1, PO=1

## Slide 59
Input/Output Organization 59
Overview
Peripheral Devices
Input-Output Interface
Asynchronous Data Transfer
Modes of Transfer
Priority Interrupt
Direct Memory Access
Input-Output Processor

## Slide 60
Input/Output Organization 60
Direct Memory Access
Block of data transfer between high speed devices like Disk and Memory
* DMA controller - Interface which takes over the buses to manage the transfer directly between
  Memory and I/O Device, freeing CPU for other tasks
* CPU initializes DMA Controller by sending memory address and the block size (number of words)

## Slide 61
Input/Output Organization 61
Direct Memory Access
Data bus
Read
Write
ABUS
DBUS
RD
WR
Bus request
Bus granted
BR
BG
CPU
Data bus
DMA select
Read
Write
Bus request
Bus grant
Interrupt
DS
RS
RD
WR
BR
BG
Interrupt
Data bus
buffers
Address bus
buffers
Address register
Word count register
Control register
DMA request
DMA acknowledge
to I/O device
Control
logic
Internal Bus
Fig 2: Block diagram of DMA controller
Fig 1: CPU bus signals for DMA transfer (Bus control by DMA)
Address bus
Address register:
Contains an address to specify
Desired location in memory
Word count register
Holds no. of words to be transferred
Control register
Specifies the mode of transfer

## Slide 62
Input/Output Organization 62
DMA Transfer can be made in several ways
Burst Transfer :
a block sequence consisting of memory words is transferred in continuous burst while the DMA controller is master of memory bus
This mode of transfer is needed for fast devices such as magnetic disk where data transmission cannot be stopped or slowed down until an entire block is transferred
Direct Memory Access
RD and WR is bidirectional
When BG=0 CPU can communicate with DMA Register (RW info.)
When BG=1 CPU left the buses and DMA can communicate directly with memory

## Slide 63
Input/Output Organization 63
(2) Cycle stealing :
Alternative technique called cycle stealing allows DMA controller to transfer one data word at time after which it must return control of the buses to the CPU.
CPU merely delays its operation for one memory cycle to allow the direct memory I/O transfer to “steal” one memory cycle
Direct Memory Access

## Slide 64
Input/Output Organization 64
DMA I/O Operation
DMA is first initialized by CPU. After that DMA starts and continues to transfer data between memory and peripheral unit until an entire block is transferred.
CPU initializes the DMA by sending following information through data bus:
    (1) Starting address of the memory block (for read/write)
    (2) Word Count (no. of words in memory block)
    (3) Control to specify mode of transfer (E.g. read/write)
    (4) A control to start DMA Transfer

## Slide 65
Input/Output Organization 65
Cycle Stealing
While DMA I/O takes place, CPU is also executing instructions
DMA Controller and CPU both access Memory -> Memory Access Conflict
Memory Bus Controller
- Coordinating the activities of all devices requesting memory access
- Priority System
Memory accesses by CPU and DMA Controller are interwoven,
with the top priority given to DMA Controller

## Slide 66
Input/Output Organization 66
Cycle Stealing
Cycle Steal
- CPU is usually much faster than I/O(DMA), thus CPU uses the most of the memory cycles
- DMA Controller steals the memory cycles from CPU
- For those stolen cycles, CPU remains idle
- For those slow CPU, DMA Controller may steal most of the memory
cycles which may cause CPU remain idle long time

## Slide 67
Input/Output Organization 67
DMA Transfer
BG
BR
CPU
RD
WR
Addr
Data
Interrupt
Random-access
memory unit (RAM)
RD
WR
Addr
Data
BR
BG
RD
WR
Addr
Data
Interrupt
DS
RS
DMA
Controller
I/O
Peripheral
device
DMA request
DMA ack.
Read control
Write control
Data bus
Address bus
Address
select

## Slide 68
Input/Output Organization 68
I/O Processor - Channel
Channel
- Processor with direct memory access capability that communicates with I/O devices
- Channel accesses memory by cycle stealing
- Unlike DMA Controller, IOP can fetch and execute its own instruction
- IOP Instructions (Commands) specially designed to facilitate I/O transfer.
PD
PD
PD
PD
Peripheral devices
I/O bus
Input-output
processor
(IOP)
Central
processing
unit (CPU)
Memory
unit
Memory Bus

## Slide 69
Input/Output Organization 69
I/O Processor - Channel
- Data gathered in IOP at device rate and bit capacity while CPU executing own program
- Transfer between IOP and Device similar to Programmed I/O and
transfer between IOP and Memory similar to DMA
- CPU is master while IOP is slave processor
- CPU initiates the channel by executing a channel I/O class instruction and once initiated, channel operates independent of the CPU
PD
PD
PD
PD
Peripheral devices
I/O bus
Input-output
processor
(IOP)
Central
processing
unit (CPU)
Memory
unit
Memory Bus

## Slide 70
Input/Output Organization 70
Channel CPU Communication
Send instruction
to test IOP.path
If status OK, then send
start I/O instruction
to IOP.
CPU continues with
another program
Transfer status word
to memory
Access memory
for IOP program
Conduct I/O transfers
using DMA;
Prepare status report.
I/O transfer completed;
Interrupt CPU
Request IOP status
Transfer status word
to memory location
Check status word
for correct transfer.
Continue
CPU operations
IOP operations